## Slide 1: Two-Layer Contactless Physical Authentication System: Combining Facial & Voice Recognition
Group Members:
Abdullah Laeeq (CIIT/FA22-BCE-026/LHR)
Ali Hamza (CIIT/FA22-BCE-071/LHR)
Muhammad Faizan Shurjeel (CIIT/FA22-BCE-086/LHR)
Supervisor: Dr. Zaid Ahmad
Co-Supervisor: Engr. Talha Naveed
Department of Computer Engineering
COMSATS University Islamabad (Lahore Campus)
September 2025

## Slide 2: Introduction: The Shifting Landscape of Identity Verification
The Dual Challenge of Modern Authentication:
1. The Crisis in Digital & Physical Trust:
• Systemic Vulnerabilities: Traditional credentials like passwords and PINs are fundamentally broken, consistently compromised by data breaches and sophisticated phishing attacks
• The Rise of Spoofing: Single-biometric systems face new threats. High-quality masks, deepfake videos, and voice recordings can potentially deceive isolated facial or voice recognition systems
2. The Post-Pandemic Imperative for Hygiene:
• Contact as a Vector: The global health crisis has permanently shifted our perception of shared surfaces. Contact-based biometrics are now recognized as vectors for germ transmission
• Demand for Touchless Interaction: Clear market and societal need for solutions that eliminate physical contact
Our Proposed Paradigm: A Synergistic Solution:
1. The Synergy of Face & Voice:
• Exponentially Increased Security: We combine two distinct biometric markers. An attacker would need to successfully spoof both appearance and voice characteristics simultaneously
• Resilience Through Duality: A failure or spoof on one layer is caught by the other, creating a robust and fault-tolerant system
2. Democratizing Advanced Security:
• Accessibility and Affordability: Engineering a solution that is not proprietary or expensive
• By targeting cost-effective embedded hardware, we make high-security, multi-modal authentication accessible to diverse environments
Project Vision: To engineer a robust, efficient, and accessible two-layer authentication system that addresses the core security and hygiene challenges of today.

## Slide 3: Literature Review - Facial Recognition
Evolution of Facial Recognition:
• Transition from classical methods (Eigenfaces) to Deep Learning
• Deep CNNs now dominate, achieving near-perfect accuracy
Key Architectural Approaches:
• FaceNet (Google): Foundational model using InceptionResNetV1 architecture
- Creates unique "facial embedding" vector representation
• ArcFace: State-of-the-art approach with Additive Angular Margin Loss
- Superior accuracy in distinguishing similar-looking faces
Our Strategy:
• Starting Point: FaceNet (well-documented, foundational)
• Proposed Upgrade: ArcFace for superior accuracy

## Slide 4
Facial Recognition Comparison
Feature | FaceNet (InceptionResNetV1) | ArcFace
Core Concept | Triplet Loss | Additive Angular Margin Loss
Accuracy | High (Baseline) | Very High (State-of-the-Art)
Key Advantage | Well-documented, foundational | Superior separation of identities
Our Choice | Starting Point | Proposed Upgrade

## Slide 5: Literature Review - Voice Recognition
Focus: Speaker Verification vs. Speech Recognition
• Our project focuses on Speaker Verification: Identifying WHO is speaking, not WHAT they are saying
Key Architectural Approaches:
• x-vectors: Deep neural network approach creating fixed-length "speaker embedding"
- Represents unique voice characteristics from variable-length audio
• ECAPA-TDNN: Evolution of x-vectors with attention mechanisms
- More robust to noise and achieves higher accuracy
- Focuses on most important speech frames
Our Choice:
• Proposed Model: ECAPA-TDNN using SpeechBrain toolkit
• State-of-the-art accuracy and robustness

## Slide 6
Voice Recognition Comparison
Feature | x-vector | ECAPA-TDNN
Core Concept | Deep Neural Network Embeddings | Time Delay Neural Network with Attention
Accuracy | Good | Excellent (State-of-the-Art)
Key Advantage | Efficient and widely used | Highly robust and accurate
Our Choice | Baseline | Proposed Model

## Slide 7: Objectives
Completed:
• Extensive literature review of facial and speaker verification models
• Preliminary selection of AI models (FaceNet/ArcFace, ECAPA-TDNN)
• Analysis of hardware constraints and identification of MVP platforms
• Definition of high-level system architecture
In Progress / To Be Completed:
1. Develop and benchmark facial recognition pipeline on PC
2. Develop and benchmark voice recognition pipeline on PC
3. Integrate both pipelines with decision fusion engine
4. Implement anti-spoofing (liveness detection) mechanisms
5. Optimize and port complete software to target embedded platform
6. Conduct performance evaluation using standard metrics (FAR, FRR)

## Slide 8: Methodology - High-Level Architecture
Our system is designed as a modular pipeline:
1. User Interfacing & Sensors:
• Camera and microphone capture user's biometric data
2. Data Ingestion & Allocation:
• Raw data is pre-processed
• Video stream → Face pipeline
• Audio stream → Voice pipeline
3. Parallel AI Pipelines:
• Facial and Voice Recognition pipelines run independently
• Generate unique embeddings for each modality
4. Authentication Core:
• Fusion engine compares new embeddings against stored templates
• Considers anti-spoofing results
• Makes final authentication decision
5. Backend Services:
• Based on decision, performs action (unlock door, log event, etc.)

## Slide 9: Methodology - AI Pipeline Details
Facial Recognition Pipeline:
1. Input: Live video frame
2. Face Detection: Lightweight detector (RetinaFace) finds face in frame
3. Pre-processing: Face is cropped, aligned, and normalized
4. Feature Extraction: Recognition model (ArcFace) generates 512-dimension embedding
5. Comparison: New embedding compared to stored embedding using cosine similarity
Voice Recognition Pipeline:
1. Input: Live audio stream
2. Pre-processing: Audio converted to required format (16kHz, mono)
3. Feature Extraction: ECAPA-TDNN processes audio to generate 192-dimension embedding
4. Comparison: New embedding compared to stored embedding
Key Output: Unique numerical signatures (embedding vectors) for each modality

## Slide 10: Methodology - Hardware & Anti-Spoofing
Crucial Addition: Liveness Detection (Anti-Spoofing)
• Prevents attacks using photos or videos
• Proposed Method: Eye-blink detection algorithm
• Simple but effective initial check for live person
Hardware Development Strategy:
Phase 1 (PC Development):
• Entire system built and tested on standard PC
• Ensures functionality before hardware constraints
Phase 2 (MVP Deployment) - Two cost-effective paths:
Option A (Preferred/Innovative):
• Repurpose older Android smartphone
• Leverage ARM processor, camera, and microphone
• Run AI backend in Linux environment (e.g., Termux)
Option B (Contingency):
• Refurbished Mini-PC (e.g., Dell OptiPlex)
• Stable and predictable alternative

## Slide 11
SDG Mapping
SDG Goal | Inclusion Level | Project's Contribution | How Goal is Met
SDG 9: Industry, Innovation, and Infrastructure | Major | Develop resilient, secure, and innovative authentication infrastructure | Novel, accessible, and affordable security system fostering innovation in physical and digital security

## Slide 12
Project Timeline
Milestone | Description | Starting Week | Duration (Weeks)
1 | Finalize Requirements & Detailed System Design | Week 1 | 1
2 | Environment Setup & Data Collection Protocol | Week 2 | 1
3 | Development of Facial Recognition Module | Week 3 | 3
4 | Development of Voice Recognition Module | Week 4 | 3
5 | Integration of Both Modules & Fusion Engine | Week 7 | 2
6 | Implementation of Liveness Detection | Week 9 | 2
7 | System Optimization & Porting to MVP Hardware | Week 11 | 3
8 | Testing, Evaluation & Final Report Writing | Week 14 | 2

## Slide 13: References
Key References:
• Schroff, F., Kalenichenko, D., & Philbin, J. (2015). FaceNet: A Unified Embedding for Face Recognition and Clustering. 2015 IEEE Conference on Computer Vision and Pattern Recognition (CVPR).
• Deng, J., Guo, J., Xue, N., & Zafeiriou, S. (2019). ArcFace: Additive Angular Margin Loss for Deep Face Recognition. 2019 IEEE/CVF Conference on Computer Vision and Pattern Recognition (CVPR).
• Ravanelli, M., et al. (2021). SpeechBrain: A General-Purpose Speech Toolkit. arXiv preprint arXiv:2106.04624.
• Desplanques, B., Thienpondt, J., & Demuynck, K. (2020). ECAPA-TDNN: Emphasized Channel Attention, Propagation and Aggregation in TDNN Based Speaker Verification. 2020 IEEE International Conference on Acoustics, Speech and Signal Processing (ICASSP).
• Chi, Jin, et al. (2020). RetinaFace: Single-Shot Multi-Level Face Localisation in the Wild. 2020 IEEE/CVF Conference on Computer Vision and Pattern Recognition (CVPR).